## Slide 1
1
Digital Logic Design
Farhana Akter Suci, Lecturer, Uttara University
Topic: 4-bit Parallel Adder-Subtractor
Farhana Akter Suci
Lecturer, Uttara University

## Slide 2
2
4-bit Parallel Adder
Farhana Akter Suci, Lecturer, Uttara University
Consider a circuit to add two 4-bit numbers together and a carry-in, to produce a 5-bit result:
4-bit
Parallel Adder
C4
C0
X1
X0
Y3
Y2
S3
S2
S1
S0
Y1
Y0
X3
X2
5-bit result is sufficient because the largest result is:
(1111)2+(1111)2+(1)2 = (11111)2
Black-box view of 4-bit parallel adder

## Slide 3
3
4-bit Parallel Adder
Farhana Akter Suci, Lecturer, Uttara University
SSI design technique should not be used.
Truth table for 9 inputs very big, i.e. 29=512 entries:
X3X2X1X0 | Y3Y2Y1Y0 | C0 | C4 | S3S2S1S0
0 0 0 0 | 0 0 0 0 | 0 | 0 | 0 0 0 0
0 0 0 0 | 0 0 0 0 | 1 | 0 | 0 0 0 1
0 0 0 0 | 0 0 0 1 | 0 | 0 | 0 0 0 1
… | … | … | … | …
0 1 0 1 | 1 1 0 1 | 1 | 1 | 0 0 1 1
… | … | … | … | …
1 1 1 1 | 1 1 1 1 | 1 | 1 | 1 1 1 1
Simplification very complicated as no. of input is 9 so 512(=29) possible combination will be there in truth table!

## Slide 4
4
4-bit Parallel Adder
Farhana Akter Suci, Lecturer, Uttara University
Alternative design possible.
Addition formula for each pair of bits (with carry in),
Ci+1Si = Xi + Yi + Ci
has the same function as a full adder.
Ci+1 = Xi Yi + (Xi ⊕ Yi ) Ci
Si = Xi ⊕ Yi ⊕ Ci
NB: Similar to FA equation
C = XY + (X⊕Y)Z
S = (X⊕Y)⊕Z
In plain English
Each bit position just adds two input bits plus whatever carry rolled in from the position before it, producing one sum bit and one carry-out bit — that's exactly what a full adder does.

## Slide 5
5
4-bit Parallel Adder
Farhana Akter Suci, Lecturer, Uttara University
Cascading 4 full adders via their carries, we get:
Output
Input
n-bit parallel adder requires n full- adders

## Slide 6
6
Examples
Farhana Akter Suci, Lecturer, Uttara University
Simple examples using 4-bit parallel adder as building blocks:
  Adder cum Subtractor
  16-Bit Parallel Adder
  BCD to excess 3 code converter

## Slide 7
7
4-bit Parallel Adder-Subtractor
Farhana Akter Suci, Lecturer, Uttara University
Subtraction can be performed through addition using 2s-complement numbers.
Hence, we can design a circuit which can perform both addition and subtraction, using a parallel adder.
4-bit
Parallel Adder
S: control signal for add/subtract
X1
X0
Y3
Y2
Result: either X+Y or X-Y
Y1
Y0
X3
X2

## Slide 8
8
4-bit Parallel Adder-Subtractor
Farhana Akter Suci, Lecturer, Uttara University
Design requires:
(i) XOR gates:
S = 0
Y
Y
S = 1
Y’
Y
such that: output = Y when S=0
= Y' when S=1
(ii) S connected to carry-in.
S | Y | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 9
9
4-bit Parallel Adder-Subtractor
Farhana Akter Suci, Lecturer, Uttara University
Adder cum subtractor circuit:
Analysis:
If S=1, then
X + (1's complement of Y) +1
appears as the result.
If S=0, then X+Y appears as
the result.

## Slide 10
10
Example
Farhana Akter Suci, Lecturer, Uttara University
Applications: Condition Based Adder Subtractor
Design a circuit that takes two binary number A, B and performs A-B, if certain condition is met or else perform A+B
Two Methods
Brute Force Approach: Find the minterms and use the SOP(s) directly
Smart Approach: Find existing patterns within the SOP(s)

## Slide 11
11
Example
Farhana Akter Suci, Lecturer, Uttara University
Build a calculator that can add or subtract two 4-bit numbers: X and Y. Now, if both of the numbers are greater than or equal to 8, then the calculator will do the operation X+Y (addition). Otherwise, the calculator will do the operation X-Y(subtraction). Design the circuit using a 4-bit parallel adder-subtractor.

## Slide 12
12
Example
Farhana Akter Suci, Lecturer, Uttara University
Perform A-B, if B is Divisible by 12 using Brute Force Approach
Only the numbers 0 and 12 are divisible by 12 among all 4-bit numbers, So the following expression will solve the problem,
F(B3,B2,B1,B0) = B3B2B1'B0' + B3'B2'B1'B0'
If the number of minterm increases, you may use KMAP to simplify the circuit.
Minterm | Product
0 | B3’B2’B1’B0’
12 | B3B2B1’B0’

## Slide 13
13
Example
Farhana Akter Suci, Lecturer, Uttara University
Perform A-B, if B is Divisible by 12 using Patterns
Possible combinations among B3 and B2 are 00 and 11, hence XNOR gate was used to combine them as only XNOR gate will provide 1 for these two unique combinations. NOR gate was used for latter variables for the same reason.
Finally, combining them with AND gate ensures the output of the AND gate will only be 1 if the current combination is indeed divisible by 12. If C0 receives 1 then it will perform A-B.

## Slide 14
14
Example
Farhana Akter Suci, Lecturer, Uttara University
Perform A-B, if B is Divisible by 12 using Patterns (Cont)
The solution is simulated for both valid combinations who are divisible by 12, 0000 and 1100. The red circled elements indicate that the output of the intermediary gates cannot mismatch, any mismatch in those circled outputs means that the current combination is not divisible by 12 and the final output will give 0 which will result in C0 being 0 hence, performing A+B likewise

## Slide 15
15
Example
Farhana Akter Suci, Lecturer, Uttara University
Perform A-B, if B is Divisible by 12 using Patterns (Alternate Solution)
The alternate solution using different logic gates also fulfill the same logic

## Slide 16
16
16-bit Parallel Adder
Farhana Akter Suci, Lecturer, Uttara University
Larger parallel adders can be built from smaller ones.
Example: a 16-bit parallel adder can be constructed from four 4-bit parallel adders:
X15…X12
X11…X8
X7…X4
X3…X0
Y15…Y12
Y11…Y8
Y7…Y4
Y3…Y0

## Slide 17
17
16-bit Parallel Adder
Farhana Akter Suci, Lecturer, Uttara University
Shortened notation for multiple lines.
16-bit parallel adder ripples carry from one 4-bit block to the next.
Such ripple-carry circuits are “slow” because of long delays needed to propagate the carries.
4
S3 .. S0
S3 S2 S1 S0
is a shortened notation for

## Slide 18
18
Arithmetic Circuits: Cascading Adders
Farhana Akter Suci, Lecturer, Uttara University
Application: 6-person voting system.
Use FAs and a 4-bit binary parallel adder.
Each FA can sum up to 3 votes.

## Slide 19
19
Try it yourself
Farhana Akter Suci, Lecturer, Uttara University
Example: Using Full adders and 4 Bit Parallel Adder,
Design a 12 person voting system
Design a 13 person voting system, your circuit must be efficient.
Design a 14 person voting system
Using Half Adder and 4 Bit Parallel Adder
Design 10 person voting system. Your circuit must be efficient

## Slide 20
20
Solution of 1
Farhana Akter Suci, Lecturer, Uttara University
Design a 12 person voting system

## Slide 21
21
BCD to excess 3 code converter
Farhana Akter Suci, Lecturer, Uttara University
Think:
A code converter that will take 4 bit BCD code as input and generate the Excess 3 output using 4 bit parallel adder.

## Slide 22
22
BCD to excess 3 code converter
Farhana Akter Suci, Lecturer, Uttara University
Solution:
Inspection of truth table of ‘excess 3 from BCD’ shows that we can get excess-3 code from BCD by adding ‘0011’ to each BCD number. This addition can be implemented by means of 4-bit full adder MSI circuit.
Let, ABCD as BCD input and WXYZ as Excess 3 output

## Slide 23
23
BCD to excess 3 code converter
Farhana Akter Suci, Lecturer, Uttara University
Solution:
Let, ABCD as BCD input and WXYZ as Excess 3 output

## Slide 24
24
Code converters – take an input code, translate to its equivalent output code.
Code Converters
Farhana Akter Suci, Lecturer, Uttara University
Code
converter
Input
code
Output
code
Example: BCD to Excess-3 Code Converter.
Input: BCD digit
Output: Excess-3 digit

## Slide 25
25
An overflow condition can be detected by observing the carry into the sign bit position (C3) and the carry out of the sign bit position (C4).
If these two carries are not equal, an overflow has occurred.
The two carries are applied to an exclusive-OR gate(XOR), an overflow is detected when the output(V) of the XOR gate is equal to 1.
Farhana Akter Suci, Lecturer, Uttara University
Overflow Detection [Self Study]
Carry: 0 1
+7 0 111
+6 0 110
____ _____
+48 1 101
Carry: 1 0
-7 1 001
-6 1 010
____ _____
-13 0 011
Carry: 1 1
-3 1 101
-2 1 110
____ _____
-5 1 011
Carry: 0 0
+2 0 010
- 4 1 100
____ _____
-2 1 110
Overflow
Overflow
No Overflow
No Overflow

## Slide 26
26
Overflow Detection [Self Study]
Farhana Akter Suci, Lecturer, Uttara University
Figure: 4-bit Adder-Subtractor with Overflow Detection
Full Adder
Full Adder
Full Adder
Full Adder

## Slide 27
27
Summary & Key Takeaways
Farhana Akter Suci, Lecturer, Uttara University
A 4-bit parallel adder chains four full adders through their carries, so an n-bit adder always needs n full adders.
Subtraction reuses the same adder: XOR gates controlled by signal S flip Y into its 1's complement, and S feeds the carry-in, so X + Y' + 1 gives X − Y (2's-complement trick).
Bigger adders scale up by cascading smaller blocks — four 4-bit adders form a 16-bit adder — but ripple-carry designs get slower as carries propagate down the chain.
Conditional add/subtract circuits (e.g. "subtract only if divisible by 12") are built by feeding a logic expression of the inputs into the carry-in/control line.
The same adder building block also powers code converters (e.g. BCD → Excess-3, adding 0011) and overflow detection (XOR of the last two carries, C3 ⊕ C4).