## Slide 1
1
0
1
1
0
LECTURE SHEET · DIGITAL LOGIC DESIGN
Half Adder
The simplest arithmetic circuit — adding two binary bits with just two logic gates.
Department of Computer Science and Engineering

## Slide 2
01 · INTRODUCTION
What is a Half Adder?
A half adder is the simplest arithmetic combinational circuit. It adds two single binary digits, X and Y, and produces two outputs:
Sum (S) — the result bit, and Carry (C) — the overflow bit, exactly as when adding two digits by hand.
It's called a “half” adder because it cannot accept a carry-in from a previous addition — only the full adder can do that.
BLOCK DIAGRAM
X
Y
HA
S
C
X + Y → Carry Sum
Half Adder | Digital Logic Design
2

## Slide 3
02 · BEHAVIOR
Truth Table
Four possible input combinations for two bits — the Sum is 1 only when exactly one input is 1; the Carry is 1 only when both inputs are 1.
Sum = XOR(X, Y)
Carry = AND(X, Y)
Reading the pattern: Sum behaves like a difference-detector (1 when bits differ), Carry behaves like an overlap-detector (1 when both are set).
X | Y | Sum (S) | Carry (C)
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Half Adder | Digital Logic Design
3

## Slide 4
03 · DERIVATION
Boolean Expressions
From the truth table, the Sum-of-Products (SOP) expression is written directly from the rows where the output is 1, then simplified:
CARRY
C = X · Y
AND of the two inputs
SUM
S = X'Y + XY' = X ⊕ Y
Simplifies to Exclusive-OR (XOR)
Why this matters: because both outputs reduce to a single 2-input gate each, a half adder needs only 2 gates total — one XOR for the Sum, one AND for the Carry.
Half Adder | Digital Logic Design
4

## Slide 5
04 · CIRCUIT
Logic Diagram
The Boolean expressions translate directly into hardware: one XOR gate produces the Sum, and one AND gate — fed the same two inputs — produces the Carry.
X, Y → same two inputs feed both gates in parallel — Sum and Carry are computed independently, with no dependency between them.
Half Adder | Digital Logic Design
5

## Slide 6
05 · EXAMPLE
Worked Example
Add the bits X = 1 and Y = 1 using half-adder logic:
CARRY
C = X · Y = 1 · 1 = 1
SUM
S = X ⊕ Y = 1 ⊕ 1 = 0
RESULT
1 + 1 = 10
Carry bit = 1, Sum bit = 0 — exactly matching ordinary binary addition.
Half Adder | Digital Logic Design
6

## Slide 7
06 · IMPLEMENTATION
Alternate Gate Implementations
Real chips are often built from a single gate family to simplify manufacturing. A half adder can also be built entirely from NAND gates or entirely from NOR gates:
Implementation | Gates Used | Gate Count
Basic (XOR + AND) | 1 XOR, 1 AND | 2 gates
Using only NAND gates | 5 NAND gates | 5 gates
Using only NOR gates | 5 NOR gates | 5 gates
WHY IT MATTERS
Fabs often standardize on one gate type (e.g. NAND) since it's a universal gate — any Boolean function, including XOR and AND, can be built from NAND alone.
Half Adder | Digital Logic Design
7

## Slide 8
07 · LIMITATION
Half Adder vs. Full Adder
A half adder can only combine two bits at a time — it has no third input for a carry produced by a previous column. This is exactly what the full adder solves.
Feature | Half Adder | Full Adder
Inputs | 2 (X, Y) | 3 (X, Y, Carry-in)
Outputs | 2 (Sum, Carry) | 2 (Sum, Carry-out)
Gates needed | 1 XOR + 1 AND | 2 XOR + 2 AND + 1 OR
Handles carry-in? | No | Yes
Use case | Least-significant bit pair | Higher-order bits in a multi-bit adder
Half Adder | Digital Logic Design
8

## Slide 9
08 · USES
Applications
1
Full Adder Building Block
Two half adders + one OR gate form a complete full adder.
2
Multi-bit Adders
Forms the least-significant-bit stage of ripple-carry and parallel adders.
3
ALUs
Used inside processor Arithmetic Logic Units for bit-level addition.
4
Counters & Incrementers
Applied in digital counter and increment circuits.
5
Bit Comparison
XOR output also flags whether two bits differ from each other.
6
Teaching Foundation
The starting point for understanding all combinational arithmetic circuits.
Half Adder | Digital Logic Design
9

## Slide 10
SUMMARY
Key Takeaways
Half adder = 1 XOR gate (Sum) + 1 AND gate (Carry).
Adds exactly two bits; produces a Sum and a Carry.
S = X ⊕ Y, C = X · Y
Cannot accept a carry-in — cannot be chained for multi-bit addition alone.
Two half adders + one OR gate combine to form a full adder.
Department of Computer Science and Engineering