## Slide 1
Lecture 6
Adder-Subtractor with Applications
Department of Computer Science and Engineering, Uttara University
CSE0613203 : Digital Logic Design

## Slide 2
2
The combinational circuit that performs the addition of two bits is called a half-adder.
If the bits are X and Y, we will get C (Carry) & S (Sum)
X
+ Y
C S
Half Adder
Department of Computer Science and Engineering
Half
Adder
X
Y
S
C
(X + Y)

## Slide 3
3
Now, we draw the truth table for all possible input combinations
0 0
+ 0 + 1
0 0 0 1
1 1
+ 0 + 1
0 1 1 0
Half Adder
Department of Computer Science and Engineering
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 4
4
From the truth table, we find out the SOP to get the boolean function & simplify it.
C = XY
S = X'Y + XY' = X⊕Y
Half Adder
Department of Computer Science and Engineering
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Now, we draw the logic diagram.

## Slide 5
5
Half-adder adds up only two bits.
To add two binary numbers, we need to add 3 bits (including the carry).
Example:
Need Full Adder (so called as it can be made from two half-adders).
Full Adder
Department of Computer Science and Engineering
Full
Adder
X
Y
Z
S
C
(X + Y + Z)

## Slide 6
6
From the truth table, we find out the SOP to get the boolean function & simplify it.
Full Adder
Department of Computer Science and Engineering
X | Y | Z | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Note:
Z - carry in (to the current position)
C - carry out (to the next position)
C = X’YZ + XY’Z + XYZ’ + XYZ
S = X'Y'Z + XYZ + X'YZ' + XY'Z'

## Slide 7
7
Simplifying,
C = X’YZ + XY’Z + XYZ’ + XYZ
= Z (X’Y + XY’) + XY (Z + Z’)
= Z (X ⊕ Y) + XY
S = X’Y’Z + X’YZ’ + XY’Z’ + XYZ
= X’ (Y’Z + YZ’) + X (Y’Z’ + YZ)
= X’ (Y⊕ Z) + X (Y⊕ Z)’ [(Y ⊕ Z) = A]
= X’A + XA’
= X ⊕ A
= X ⊕ Y ⊕ Z
Full Adder
Department of Computer Science and Engineering

## Slide 8
8
Circuit
Full Adder
Department of Computer Science and Engineering

## Slide 9
9
Full Adder made from two Half-Adders (+ OR gate).
Why It Is Called Full Adder?
Department of Computer Science and Engineering

## Slide 10
10
4-bit Parallel Adder
Department of Computer Science and Engineering
Consider a circuit to add two 4-bit numbers together and a carry-in, to produce a 5-bit result:
4-bit
Parallel Adder
C4
C0
X1
X0
Y3
Y2
S3
S2
S1
S0
Y1
Y0
X3
X2
5-bit result is sufficient because the largest result is:
(1111)2+(1111)2+(1)2 = (11111)2
Black-box view of 4-bit parallel adder

## Slide 11
11
4-bit Parallel Adder
Department of Computer Science and Engineering
SSI design technique should not be used.
Truth table for 9 inputs very big, i.e. 29=512 entries:
X3X2X1X0 | Y3Y2Y1Y0 | C0 | C4 | S3S2S1S0
0 0 0 0 | 0 0 0 0 | 0 | 0 | 0 0 0 0
0 0 0 0 | 0 0 0 0 | 1 | 0 | 0 0 0 1
0 0 0 0 | 0 0 0 1 | 0 | 0 | 0 0 0 1
… | … | … | … | …
0 1 0 1 | 1 1 0 1 | 1 | 1 | 0 0 1 1
… | … | … | … | …
1 1 1 1 | 1 1 1 1 | 1 | 1 | 1 1 1 1
Simplification very complicated as no. of input is 9 so 512(=29) possible combination will be there in truth table!

## Slide 12
12
4-bit Parallel Adder
Department of Computer Science and Engineering
Alternative design possible.
Addition formula for each pair of bits (with carry in),
Ci+1Si = Xi + Yi + Ci
has the same function as a full adder.
Ci+1 = Xi Yi + (Xi ⊕ Yi ) Ci
Si = Xi ⊕ Yi ⊕ Ci
NB: Similar to FA equation
C = XY + (X⊕Y)Z
S = (X⊕Y)⊕Z

## Slide 13
13
4-bit Parallel Adder
Department of Computer Science and Engineering
Cascading 4 full adders via their carries, we get:
Output
Input
n-bit parallel adder requires n full- adders

## Slide 14
14
Examples
Department of Computer Science and Engineering
Simple examples using 4-bit parallel adder as building blocks:
  Adder cum Subtractor
  16-Bit Parallel Adder
  BCD to excess 3 code converter

## Slide 15
15
4-bit Parallel Adder-Subtractor
Department of Computer Science and Engineering
Subtraction can be performed through addition using 2s-complement numbers.
Hence, we can design a circuit which can perform both addition and subtraction, using a parallel adder.
4-bit
Parallel Adder
S: control signal for add/subtract
X1
X0
Y3
Y2
Result: either X+Y or X-Y
Y1
Y0
X3
X2

## Slide 16
16
4-bit Parallel Adder-Subtractor
Department of Computer Science and Engineering
Design requires:
(i) XOR gates:
S = 0
Y
Y
S = 1
Y’
Y
such that: output = Y when S=0
= Y' when S=1
(ii) S connected to carry-in.
S | Y | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 17
17
4-bit Parallel Adder-Subtractor
Department of Computer Science and Engineering
Adder cum subtractor circuit:
Analysis:
If S=1, then
X + (1's complement of Y) +1
appears as the result.
If S=0, then X+Y appears as
the result.

## Slide 18
18
Example
Department of Computer Science and Engineering
Applications: Condition Based Adder Subtractor
Design a circuit that takes two binary number A, B and performs A-B, if certain condition is met or else perform A+B
Two Methods
Brute Force Approach: Find the minterms and use the SOP(s) directly
Smart Approach: Find existing patterns within the SOP(s)

## Slide 19
19
Example
Department of Computer Science and Engineering
Build a calculator that can add or subtract two 4-bit numbers: X and Y. Now, if both of the numbers are greater than or equal to 8, then the calculator will do the operation X+Y (addition). Otherwise, the calculator will do the operation X-Y(subtraction). Design the circuit using a 4-bit parallel adder-subtractor.

## Slide 20
20
Example
Department of Computer Science and Engineering
Perform A-B, if B is Divisible by 12 using Brute Force Approach
Only the numbers 0 and 12 are divisible by 12 among all 4-bit numbers, So the following expression will solve the problem,
F(B3,B2,B1,B0) = B3B2B1'B0' + B3'B2'B1'B0'
If the number of minterm increases, you may use KMAP to simplify the circuit.
Minterm | Product
0 | B3’B2’B1’B0’
12 | B3B2B1’B0’

## Slide 21
21
Example
Department of Computer Science and Engineering
Perform A-B, if B is Divisible by 12 using Patterns
Possible combinations among B3 and B2 are 00 and 11, hence XNOR gate was used to combine them as only XNOR gate will provide 1 for these two unique combinations. NOR gate was used for latter variables for the same reason.
Finally, combining them with AND gate ensures the output of the AND gate will only be 1 if the current combination is indeed divisible by 12. If C0 receives 1 then it will perform A-B.

## Slide 22
22
Example
Department of Computer Science and Engineering
Perform A-B, if B is Divisible by 12 using Patterns (Cont)
The solution is simulated for both valid combinations who are divisible by 12, 0000 and 1100. The red circled elements indicate that the output of the intermediary gates cannot mismatch, any mismatch in those circled outputs means that the current combination is not divisible by 12 and the final output will give 0 which will result in C0 being 0 hence, performing A+B likewise

## Slide 23
23
Example
Department of Computer Science and Engineering
Perform A-B, if B is Divisible by 12 using Patterns (Alternate Solution)
The alternate solution using different logic gates also fulfill the same logic

## Slide 24
24
16-bit Parallel Adder
Department of Computer Science and Engineering
Larger parallel adders can be built from smaller ones.
Example: a 16-bit parallel adder can be constructed from four 4-bit parallel adders:
X15…X12
X11…X8
X7…X4
X3…X0
Y15…Y12
Y11…Y8
Y7…Y4
Y3…Y0

## Slide 25
25
16-bit Parallel Adder
Department of Computer Science and Engineering
Shortened notation for multiple lines.
16-bit parallel adder ripples carry from one 4-bit block to the next.
Such ripple-carry circuits are “slow” because of long delays needed to propagate the carries.
4
S3 .. S0
S3 S2 S1 S0
is a shortened notation for

## Slide 26
26
Arithmetic Circuits: Cascading Adders
Department of Computer Science and Engineering
Application: 6-person voting system.
Use FAs and a 4-bit binary parallel adder.
Each FA can sum up to 3 votes.

## Slide 27
27
Try it yourself
Department of Computer Science and Engineering
Example: Using Full adders and 4 Bit Parallel Adder,
Design a 12 person voting system
Design a 13 person voting system, your circuit must be efficient.
Design a 14 person voting system
Using Half Adder and 4 Bit Parallel Adder
Design 10 person voting system. Your circuit must be efficient

## Slide 28
28
Solution of 1
Department of Computer Science and Engineering
Design a 12 person voting system

## Slide 29
29
BCD to excess 3 code converter
Department of Computer Science and Engineering
Think:
A code converter that will take 4 bit BCD code as input and generate the Excess 3 output using 4 bit parallel adder.

## Slide 30
30
BCD to excess 3 code converter
Department of Computer Science and Engineering
Solution:
Inspection of truth table of ‘excess 3 from BCD’ shows that we can get excess-3 code from BCD by adding ‘0011’ to each BCD number. This addition can be implemented by means of 4-bit full adder MSI circuit.
Let, ABCD as BCD input and WXYZ as Excess 3 output

## Slide 31
31
BCD to excess 3 code converter
Department of Computer Science and Engineering
Solution:
Let, ABCD as BCD input and WXYZ as Excess 3 output

## Slide 32
32
Code converters – take an input code, translate to its equivalent output code.
Code Converters
Department of Computer Science and Engineering
Code
converter
Input
code
Output
code
Example: BCD to Excess-3 Code Converter.
Input: BCD digit
Output: Excess-3 digit

## Slide 33
33
An overflow condition can be detected by observing the carry into the sign bit position (C3) and the carry out of the sign bit position (C4).
If these two carries are not equal, an overflow has occurred.
The two carries are applied to an exclusive-OR gate(XOR), an overflow is detected when the output(V) of the XOR gate is equal to 1.
Department of Computer Science and Engineering
Overflow Detection [Self Study]
Carry: 0 1
+7 0 111
+6 0 110
____ _____
+48 1 101
Carry: 1 0
-7 1 001
-6 1 010
____ _____
-13 0 011
Carry: 1 1
-3 1 101
-2 1 110
____ _____
-5 1 011
Carry: 0 0
+2 0 010
- 4 1 100
____ _____
-2 1 110
Overflow
Overflow
No Overflow
No Overflow

## Slide 34
34
Overflow Detection [Self Study]
Department of Computer Science and Engineering
Figure: 4-bit Adder-Subtractor with Overflow Detection
Full Adder
Full Adder
Full Adder
Full Adder